## Slide 1: M3d micro
Retail: $300
Weight: 1 kg
Print Area: 109 x 113 x 116mm
  (less in top corners)
Supports most standard filament
Includes printing software
Self-calibrating

## Slide 2: Ultimaker 3
Retail: > $3500
Weight: 25 kg
Print Area: 215 x 215 x 200mm
Higher quality prints
Heated bed
Dual extrusion
  2 colors in one print
  2 materials in one print

## Slide 3: M3D CRANE QUAD
Retail: $550?
  (in pre-orders)
Full color printing!
  4 heads, mixes CMYK
  (or use four materials)
Heated bed
Print Area: 214 × 214 × 230mm

## Slide 4: Filament (3d printer "ink")
PLA – compostable plastic
ABS – Lego plastic
Flexible (e.g. "NinjaFlex")
Nylon
Carbon fiber
Wood
Metal (filled)
...and more!
Image from Adafruit catalog

## Slide 5: How does it work?
Gears feed the filament down to a heater
Filament is melted and extruded
Head moves around, building model in layers
Image from M3D support site

## Slide 6: How hot is that nozzle?
PLA – 215°C - 235°C
ABS – 230°C - 240°C
NinjaFlex – 210°C - 225°C
Nylon – 240°C - 280°C
Wood – 200°C - 260°C
Polycarbonate – 250°C - 320°C
Temperature Guide from Filaments.ca
These are in CELSIUS, so that's over
400 DEGREES FAHRENHEIT

## Slide 7: Is it safe?
  PLA (corn starch) is safest
    No toxic fumes
    Some microparticles
    No extraordinary ventilation needed
  Other filaments (including ABS)
    Varying degrees of harmful fumes
    Use in a well-ventilated area
    Some printers have filtered enclosures

## Slide 8: Thingiverse
Download or share printable files
  Or order patterns printed
Categories:
  3D Printing
  Art
  Fashion
  Gadgets
Household
Tools
Toys & Games

## Slide 9: Design your own
Parameterized designs
Remix from Thingiverse
Design software:
  OpenSCAD
  TinkerCAD
  Google Sketchup
  …

## Slide 10: Tools for printing
Painter's Tape (on bed)
  Apply to bed for easier to remove prints
Glue (on bed)
  Sticky, avoids peeling up
Tweezers
  Cleaning nozzle (very hot!)

## Slide 11: Tools for finishing
Palette knife
  Lifting prints from bed
Sandpaper
  Various grits
Files
Dremel